## Slide 1: Standart Time
Examples

## Slide 2: Example
A direct time study was taken on a manual work element using the snapback method. The regular cycle consisted of three elements, a, b, and c. Element d is an irregular element performed every five cycles.
Work element a b c d
Observed time (min) 0.56 0.25 0.50 1.10
Performance rating 100% 80% 110% 100%
Determine (a) normal time and (b) standard time for the cycle, using allowance factor of 15%.

## Slide 3: Solution
(a) Normal time:
Tn = 0.56(1.00) + 0.25(0.80) + 0.50(1.10) + 1.10(1.00)/5 = 1.53 min
(b) Standard time:
Tstd = 1.53(1 + 0.15) = 1.76 min